## Slide 1: WF on initial access with SUL for LTE-NR UL Coexistence
Huawei, HiSilicon, MediaTek, China Telecom
3GPP TSG RAN WG1 meeting #90 R1- 1714833
Prague, Czech Republic, 21 – 25 August, 2017
Agenda item: 6.1.6

## Slide 2: Background
Agreements:
Specify mechanisms for supporting supplementary Uplink frequency
  Note: SUL herein refers to the case when there is only UL resource for a carrier from NR perspective
  Use SUL as complimentary access link (including from random access point of view) to NR TDD and to NR FDD, where the UE may select PRACH resources either in the NR TDD/FDD uplink frequency or the SUL frequency.
  Note: The SUL frequency can be a frequency shared with LTE UL(at least for the case when NR spectrum is below 6 Ghz).
    Minimize impact to NR physical layer design to enable this co-existence
  Note: whether or not UE has to support simultaneous transmission on uplink frequencies is a separate discussion

## Slide 3: Proposal
NR supports for UE initial access
  RACH configuration for SUL carrier is informed to UEs prior to UE’s RACH procedure
    The configuration information is sufficient for UEs to complete RACH procedure via only SUL carrier
    It contains a RSRP threshold for each SUL carrier which facilitates UE to determine whether the SUL is used to start its RACH procedure.
    It is broadcasted in RMSI.
  The SUL carrier is the only carrier for one UE to complete its whole RACH procedure if the UE starts its RACH procedure on the SUL carrier
Sent an LS accommodating above agreement to RAN2