## Slide 1: WF on SRS sequence generation for partial overlapping
LG Electronics, Intel Corporation,
ZTE, NEC
R1-1714894
3GPP TSG RAN1 NR #90
Prague, Czech Republic, 21th – 25th Aug. 2017
Agenda Item: 6.1.2.3.5

## Slide 2: Agreements
Agreements:
NR supports at least the following SRS sequences
  LTE SRS sequences
Study further whether or not to additionally support the following for NR SRS sequence design:
  Opt-1: Truncated ZC design
    Set of [60] long ZC sequences designed for each of [5] different reference carrier bandwidths where the sequence length exceeds the carrier bandwidth before truncation
      The portion of the truncated sequence corresponds to the SRS PRB location assigned to the UE
    Ports on the same comb are separated by cyclic shifts which are repeated every n SRS REs, e.g. n=[8,12]
  Opt-2: block-wise concatenation based ZC sequence generation.
    The number of blocks (e.g. 1, 2, …) and/or block length (e.g. 4RBs, 8RBs, …) per each block is informed to UE
      Alt1. the number of blocks and/or block length are configured by network. If 1 block is configured, SRS sequence for NR is the same as LTE SRS sequence
      Alt2. Implicit signaling e.g. the number of blocks and block length are dependent on waveform. When DFT-S-OFDM is configured to UE, the number of block is one and the block length is equal to SRS BW; When CP-OFDM is configured, the number of blocks can be larger than 1.
  Opt-3: Same LTE SRS sequence generation mechanism with additional roots
To conclude during the next meeting
  Evaluations to consider at least CM/PAPR and sequence cross-correlation for the case of fully and partially overlapping SRS allocations
  Evaluations to further consider CM/PAPR for carrier bandwidths different than the reference ones

## Slide 3: Proposals
Support block-wise concatenation based ZC sequence generation.
  The number of blocks (e.g. 1, 2, …) and/or block length (e.g. 4RBs, 8RBs, …) per each block is informed to UE
    Alt1. the number of blocks and/or block length are configured by network. If 1 block is configured, SRS sequence for NR is the same as LTE SRS sequence
    Alt2. Implicit signaling e.g. the number of blocks and block length are dependent on waveform. When DFT-S-OFDM is configured to UE, the number of block is one and the block length is equal to SRS BW; When CP-OFDM is configured, the number of blocks can be larger than 1.
  The maximum number of blocks are at most 2 in NR phase 1
  FFS whether configurable ZC sequence truncation is supported.
  FFS sequence generation details per block, e.g.,
    a single UE-specific sequence ID + root offsets for all blocks or UE-specific sequence ID per block
    Different CS per block.