## Slide 1: 1714929 3GPP TSG RAN WG1 Meeting #90 Prague, Czech Republic, 21-25 Aug 2017 Agenda item 6.1.4.2.1
WF On UE Specific Scrambling for
Early Termination on DCI Blind Detection
Coherent Logix Inc., AT&T, [NTT DOCOMO, Tsofun Algorithm, McGill University,
Huawei, Nokia, LG Electronics, InterDigital], Tejas Network, CeWiT, IITM, IITH, Reliance

## Slide 2: Background
The merits of UE specific scrambling have been shown in facilitating early termination on DCI blind detection where the aim is to:
  Discern frames presenting a match/mismatch in assigned UE_ID.
  Permit early termination to minimize energy spent decoding frames presenting a mismatch in UE_ID.
  Apply Early Termination criteria alongside that with distributed CRC to maximize energy savings.
Direct mapping assigns a sequence equal in length to the C-RNTI in select frozen bit positions, based on (i) maximum Hamming distance – Tsofun [4], (ii) the most reliable subchannels after the K information bits – McGill [5]
Spread mapping places a NR Pseudo-Random Sequence initialized by the UE_ID in a subset of the frozen bit-positions, (i) beginning with the first frozen bit after block puncturing – CLX [2], (ii) including shortened bits – NTT DOCOMO [3].

## Slide 3: Benefits
The potential for latency and energy savings increases dramatically with the availability of early termination measured in terms of decoded bit position.
UE_ID frozen bit insertion enables termination in the earliest accessible bit positions given SC(L) decoding.
Performance evaluations have shown considerable gains w.r.t. latency and energy savings with UE_ID frozen bit insertion.
UE_ID frozen bit insertion for early termination is complementary to early termination afforded through distributed CRC. Block discrimination is ultimately subjected to evaluation of the final CRC.

## Slide 4: Proposal
Adopt UE specific scrambling to facilitate early termination on DCI blind detection.
Down-selection from the following options during Sept adhoc:
  Direct mapping with a sequence equal in length to the C-RNTI in select frozen bit positions, based on: maximum Hamming distance [4]
  Direct mapping with a sequence equal in length to the C-RNTI in select frozen bit positions, based on: the most reliable subchannels after the K information bits [5]
  Spread mapping placing a NR Pseudo-Random Sequence initialized by the UE_ID in a subset of the frozen bit-positions beginning with the first frozen bit after block puncturing [2]
  Spread mapping placing a NR Pseudo-Random Sequence initialized by the UE_ID in a subset of the frozen bit-positions including shortened bits [3]
  Merged solutions are not precluded
Performance will be evaluated w.r.t. the latency/energy savings due to early termination.

## Slide 5: References
R1-1702277, “Polar Code Design for DCI”, AT&T, RAN1 #88, Athens, Feb 2017
R1-1714067, “UE_ID Frozen Bit Insertion for DCI Early Block Discrimination”, Coherent Logix Inc., RAN1 #90, Aug 2017
R1-1713966, “Scrambling design for Polar codes”, NTT DOCMO, RAN1 #90, Aug 2017
R1-1712256, “Enhancement of Early Termination by placing UE-ID on Frozen Bits”, Tsofun Algorithm, RAN1 #90, Aug 2017
R1-1713316, “Blind Detection with Polar Codes”, McGill University, RAN1 #90, Aug 2017