## Slide 1: WF on power saving signal in NB-IoT
Huawei, HiSilicon,[….]
R1-1714937
3GPP TSG RAN WG1 Meeting #90
Prague, Czech Republic, August 21~25, 2017
Agenda item 5.2.7.1.1

## Slide 2: Background
In RAN1#89, it was agreed that:
  Agreements:
    A physical signal/channel indicating whether the UE needs to decode subsequent physical channel(s) is introduced, at least for idle mode paging. Candidates for the signal/channel are:
      Wake-up signal or DTX
      Go-to-sleep signal or DTX
      Wake-up signal with no DTX
      Downlink control information
      FFS whether synchronization to the camped-on cell is assumed for detecting/decoding WUS/GTS, depending on the (e)DRX cycle length
      Design details are FFS
    Connected mode DRX is FFS

## Slide 3: Proposals
For idle mode,
  In specifying a power saving physical signal to indicate whether the UE needs to decode subsequent physical channel(s) for idle mode paging, select a candidate among the following power saving physical signals:
    Wake-up signal or DTX
    Wake-up signal with no DTX
  FFS:
    Information conveyed by the physical signal
    Design of the physical signal
For connected mode,
  Either (a) “wake up signal or DTX” or (b) Dynamic indication in DCI of USS monitoring period/occasions is adopted