## Slide 1: WF on Maximum Number of PRACH Transmission
Mitsubishi Electric, …
R1-1715230
3GPP TSG RAN WG1 meeting #90
Prague, Czech Republic, 21st – 25th August, 2017
Agenda item 6.1.1.4.3

## Slide 2
Background 1
In LTE MAC layer specification TS36.321, “PREAMBLE_TRANSMISSION_COUNTER” and “preambleTransMax” are defined to indicate Random Access problem
From TS36.321 V14.3.0
If no Random Access Response or, for BL UEs or UEs in enhanced coverage for mode B operation, no PDCCH scheduling Random Access Response is received within the RA Response window, or if none of all received Random Access Responses contains a Random Access Preamble identifier corresponding to the transmitted Random Access Preamble, the Random Access Response reception is considered not successful and the MAC entity shall:
- if the notification of power ramping suspension has not been received from lower layers:
- increment PREAMBLE_TRANSMISSION_COUNTER by 1;
--- omitted ---
- else:
- if PREAMBLE_TRANSMISSION_COUNTER = preambleTransMax + 1:
- if the Random Access Preamble is transmitted on the SpCell:
- indicate a Random Access problem to upper layers;

## Slide 3
Background 2
Agreement on the UE behavior for PRACH transmit power calculation in RAN1 NR-AH#2:
The UE calculates the PRACH transmit power for the retransmission at least based on the most recent estimate pathloss and power ramping
  The pathloss is measured at least on the SS block associated with the PRACH resources/preamble subset
UE behavior when reaching the maximum power
  If the recalculated power is still at or above the Pc,max
    The UE can transmit at maximum power even if it changes its TX beam

## Slide 4
Motivation of proposal
Like LTE, NR needs the definition of the maximum transmission number and the counter or alternative definition to indicate Random Access problem. However, they are not defined yet.
The following contributions claim the necessity of them;
    R1-1712278[Mitsubishi], R1-1712358[CATT], R1-1712960[SONY],
    R1-1713130[LG Electronics], R1-1713326[Sharp],
    R1-1713381[Qualcomm], R1-1713700[MediaTek], R1-1713807[ETRI], R1-1713904[NTT DOCOMO]
There is a concern about interference to other gNBs caused by the UE behavior after reaching the maximum power.
Even if the maximum number of PRACH transmissions is defined, the transmission with the maximum power might happen many times if the UE begins PRACH transmission with relatively higher power.

## Slide 5
Proposal
NR supports one out of the following three alternatives to indicate Random Access problem.
  Alt 1: The total maximum number of transmissions, M (like LTE)
    M is NW configurable parameter
  Alt 2: The maximum number of transmissions, N*K, applied after reaching maximum power
    N is NW configurable parameter
    K corresponds to the available number of different Tx beam directions for a given UE if the UE beam correspondence is not available, and K is 1 otherwise
  Alt 3: Both of Alt1 and Alt2