## Slide 1: WF on prioritization between SRS and short PUCCH transmission in case of collision
Mitsubishi Electric, LG, ZTE, Sanechips, Nokia, NSB, Sony, InterDigital, Ericsson, [Samsung]
3GPP TSG RAN WG1 Meeting #90b
Prague, Czech Republic, 9th – 13th October, 2017
Agenda item 7.2.3.5
R1-1718985

## Slide 2: Background information
Agreement on usage of short PUCCH for beam failure recovery
Working assumption on collision rules
Confirmation of the working assumption

## Slide 3: Background information
      Agreement on support of aperiodic CSI reporting for short PUCCH from R1-1716901 (NR-AH3)
        Support A-CSI on long and short PUCCH using higher-layer PUCCH resource configuration and DCI-based triggering, [working assumption: including with Y>0]
        FFS: timing relationship relative to CSI-RS
In LTE, the following prioritization rule is supported:
  PUCCH with ACK/NACK>aperiodic SRS>PUCCH for CSI>periodic SRS

## Slide 4: Proposals
In the case of collision of SRS and short PUCCH carrying only CSI report/beam failure recover request, support the prioritization rules in the table below:
In case SRS is dropped, dropping can be partial in time domain, i.e., only those OFDM symbols that collide with short PUCCH
*If short PUCCH is supported for beam failure recovery request and collision between short PUCCH with beam failure recovery request and aperiodic/semi persistent/periodic SRS occurs, prioritize short PUCCH
**Downselect from the following
  Alt. 1: SRS is always dropped
  Alt. 2: No rule, i.e., UE can assume that this collision will not occur
  Alt. 3: Between SRS and short PUCCH, whichever is triggered earlier is dropped
 | Aperiodic SRS | Semi-persistent SRS | periodic SRS
sPUCCH with aperiodic CSI report | [TBD]** | sPUCCH | sPUCCH
sPUCCH with semi persistent CSI report | SRS | sPUCCH | sPUCCH
sPUCCH with periodic CSI report | SRS | sPUCCH | sPUCCH
sPUCCH with beam failure recover request* | sPUCCH | sPUCCH | sPUCCH