## Slide 1: Way Forward on early data transmission in NB-IoT
Huawei, HiSilicon, ….
3GPP TSG RAN WG1 Meeting #90bis
Prague, Czech Republic, 9 – 13 October 2017
Agenda item 6.2.6.1.2
R1-1719014

## Slide 2: Background
In RAN1#90, the following was agreed:
  Agreements:
    For idle mode,
      The power saving signal in a cell supports being applied to FFS between:
        All the UEs associated to a PO in the cell
        A group of more than one of the UEs associated to a PO in the cell
        Both (a) and (b)
      How many POs the power saving signal applies to from the UE perspective is FFS between
        A single PO only
        One or more than one PO (details are FFS)
      How many POs the power saving signal applies to from the eNB perspective is FFS between
        A single PO only
        One or more than one PO (details are FFS)
      The power saving signal applicable to a UE is sent on the same paging carrier as the associated subsequent physical channel(s)
Some FFS points need to be resolved in this meeting.

## Slide 3
Proposals:
From RAN1 point of view, it is feasible to support early UL data transmission in Msg3 from an NB-IoT UE using some TBS value(s) from the TBS range specified for NB-IoT in Rel-13 with a maximum total TBS of 1000 bits.
    The detailed value(s) should consider the payload size of early data packets from RAN2.
From RAN1 perspective, the physical layer design will assume eNB is not required to always provide a grant of a larger TBS for Msg3 and can decide to just provide a legacy grant for msg3 instead