## Slide 1: WF on DL measurement RS indication for non-codebook based transmission for UL MIMO
Huawei, HiSilicon, Intel, Nokia, Nokia Shanghai Bell, Ericsson, DOCOMO, MediaTek, CATT, LG Electronics, Spreadtrum, China Telecom, OPPO, Sharp, KT Corporation, Lenovo, Motorola Mobility, Samsung, Deutsche Telekom
3GPP TSG RAN WG1 Meeting #90bis R1-1719166 Prague, Czech Republic, 9-13 October 2017
Agenda: 7.2.1.3

## Slide 2: Background
Before RAN1#89, it has been agreed for non-codebook based transmission for UL MIMO:
  Support the indication of DL measurement RS for UE to calculate candidate precoder.
In RAN1#90, further progress has been achieved and it was agreed that:
For PUSCH precoder determination in non-codebook-based UL MIMO, support Alt.1, (i.e., at least SRI(s) only without TPMI indication in the UL grant) for wideband indication.
  Note: The gNB should only signal SRI(s) such that the UL precoding transmission inferred from the signaled SRI(s) can be simultaneously conducted by the UE.
  FFS details
  FFS: If sub-band indication is supported, down-select Alt. 1-3 for it

## Slide 3: Proposal
Support indicating DL measurement RS for UE to calculate UL candidate precoders for precoded AP-SRS resource via DCI
  The DL measurement RS is a CSI-RS for CSI acquisition
  Specify the following mechanism for DCI signalling:
    Using the same field for AP-SRS resource triggering
      Association between triggering state, triggered SRS resource(s) and the CSI-RS resource ID is higher layer configured
Support indicating DL measurement RS for UE to calculate UL candidate precoders for precoded P/SP-SRS resource via higher layer signalling
  The DL measurement RS is a CSI-RS for CSI acquisition
AP-SRS(s) association with P(>1)-port AP-CSI-RS:
  AP-CSI-RS can be transmitted in the same slot as the DCI containing AP-SRS trigger.
  The AP-SRS(s) is transmitted X symbols after AP-CSI-RS.
    FFS: The scope of X and whether the AP-SRS and AP-CSI-RS can be in the same slot
AP/SP/P-SRS(s) association with P(>1)-port P/SP-CSI-RS
  Timing of UL precoder calculation based on the associated CSI-RS is up to UE implementation