## Slide 1: WF on NPRACH TDD NB-IoT Design
ZTE , Sanechips ,LGE …
3GPP TSG RAN WG1 Meeting #91
Reno, USA, 27th November – 1st December 2017
Agenda item 6.2.6.3.2
R1-1721152

## Slide 2
Proposal
    TDD NPRACH supports only 3.75kHz subcarrier spacing single-tone with frequency hopping
    The frequency location for one NPRACH transmission are constrained within the configured 12 subcarriers zone
      This is same as legacy NB-IoT FDD NPRACH
    The basic unit for NPRACH preamble is G back-to-back transmitted symbol groups followed by a guard time for 1, 2, and 3 contiguous uplink subframes, for simplicity this is called mini-unit in this WF
      X mini-unit pattern(s) can be selected for one NPRACH format
      G can be selected from {2 ,3, 4} based on different mini-unit patterns
      In each mini-unit pattern, the tone hopping distance between symbol groups inside the mini-unit is chosen from {+/- 3.75kHz , +/- 22.5kHz}
      FFS Hopping of the frequency position of the mini-unit in the 12-tone NPRACH zone for each NPRACH preamble repetition is supported , FFS details
      FFS: Hopping between X mini-unit patterns for each NPRACH preamble repetition is supported, FFS details
      RAN1 is going to select mini-unit patterns for 1, 2, and 3 contiguous uplink subframes based on performance comparison
        Examples of these candidate mini-unit patterns are given in the appendix
    FFS the number of supported NPRACH format for 1, 2, and 3 contiguous uplink subframes

## Slide 3: Appendix Example mimi patterns for 1 contiguous uplink subframes

## Slide 4: Appendix Example mini-unit pattern for 1 contiguous uplink subframes

## Slide 5: Example mini pattern for 2 contiguous uplink subframes
h
i
h

## Slide 6: Mimi pattern for 2 contiguous uplink subframes

## Slide 7: Example of mini pattern options for 3 contiguous uplink subframes
ALT1: Same as mini pattern for 1 contiguous subframe but scale up the length of mini to 3 ms
ALT2: Same as mini pattern for 1 contiguous subframe but use different symbols in one symbol group