## Slide 1
3GPP TSG RAN WG1#91 R1-1721531
Reno, USA, November 27th – December 1st, 2017
Agenda item: 7.1.1
Summary on PRB Grid Offset Indication
Samsung

## Slide 2: Background
RAN4 agreed that the channel raster for <6 GHz is either 15 kHz or 100 kHz, and the channel raster for >6 GHz is 60 kHz.
RAN1 agreed that the subcarrier spacing for RMSI and CORESET for scheduling RMSI is 15 kHz or 30 kHz for <6 GHz, and 60 kHz or 120 kHz for >6 GHz.
When RMSI subcarrier spacing is twice of the channel raster (examples for <6 GHz as shown below), SS block PRB grid can be offset from RMSI RE grid by half RMSI subcarrier spacing (marked in red in the figures).
This issue can be avoided by shifting the RMSI PRB by a channel raster (marked in red in the figures), which means the PRB grid offset between SS/PBCH block and RMSI is an integer multiple of RMSI subcarrier spacing.

## Slide 3: Proposal
RAN1 assumes the PRB grid of SS/PBCH block is aligned with the RE grid of RMSI, and the PRB grid offset between SS/PBCH block and RMSI is an integer multiple of RMSI subcarrier spacing
4 bits in NR-PBCH content are used to indicate the PRB grid offset between SS/PBCH block and RMSI
    FFS in this meeting: whether or not to support joint coding (e.g., PRB grid offset + RMSI config., etc.)
    FFS in this meeting: Use of reserved values (e.g., to indicate presence of RMSI, etc.)
Send an LS to RAN4 to inform the above decision
0000 | grid offset is 0 subcarrier spacing in RMSI numerology
0001 | grid offset is 1 subcarrier spacing in RMSI numerology
0010 | grid offset is 2 subcarrier spacing in RMSI numerology
0011 | grid offset is 3 subcarrier spacing in RMSI numerology
0100 | grid offset is 4 subcarrier spacing in RMSI numerology
0101 | grid offset is 5 subcarrier spacing in RMSI numerology
0110 | grid offset is 6 subcarrier spacing in RMSI numerology
0111 | grid offset is 7 subcarrier spacing in RMSI numerology
1000 | grid offset is 8 subcarrier spacing in RMSI numerology
1001 | grid offset is 9 subcarrier spacing in RMSI numerology
1010 | grid offset is 10 subcarrier spacing in RMSI numerology
1011 | grid offset is 11 subcarrier spacing in RMSI numerology
1100 | reserved
1101 | reserved
1110 | reserved
1111 | reserved

## Slide 4: Example 1
SS SCS = 15 kHz, CORESET SCS = 15 kHz, Channel Raster = 15 kHz

## Slide 5: Example 2
SS SCS = 30 kHz, CORESET SCS = 15 kHz, Channel Raster = 15 kHz

## Slide 6: Example 3
SS SCS = 15 kHz, CORESET SCS = 30 kHz, Channel Raster = 15 kHz

## Slide 7: Example 4
SS SCS = 30 kHz, CORESET SCS = 30 kHz, Channel Raster = 15 kHz