## Slide 1: Summary of offline discussion
Ericsson
3GPP TSG RAN WG1 Meeting #92
Sanya, China, April 16th – 20nd, 2018
Agenda Item: 7.1.3.2.1
Source: Ericsson
Document for: Discussion and Decision
R1-1805764

## Slide 2: Proposal
Proposals:
To adopt the following TP for 38.213, Section 9.2.3:
A UE may transmit one or more two PUCCHs on a serving cell in different symbols within a slot of N^slot_symb as defined in [4, TS 38.211]. In case of two PUCCHs in the slot, at least one of them is based on PUCCH format 0 or 2.
Offline discussion to finalize the table based on previous agreements
Check futher offline the agreements (tx vs. configuration)

## Slide 3: Background
Working assumption:
When single-slot PUCCH overlaps with single-slot PUCCH or single-slot PUSCH in slot n for a PUCCH group,
  The UE multiplex all UCIs on either one PUCCH or one PUSCH, using the existing UCI multiplexing rule, if both following conditions are satisfied:
    If the first symbol of the earliest PUCCH(s)/PUSCH(s) among all the overlapping channels starts no earlier than symbol N1+X after the last symbol of PDSCH(s)
    If the first symbol of the earliest PUCCH(s)/PUSCH(s) among all the overlapping channels starts no earlier than N2+Y after the last symbol of PDCCHs scheduling UL transmissions including HARQ-ACK and PUSCH (if applicable) for slot n
  If at least one pair of overlapping channels does not meet the above timeline requirements, UE consider it is an error case for all UL channels in the group of overlapping channels. UE behavior is not specified.
The definition of N1 and N2 follows the same definition in current NR spec.
X and Y are non-negative integer values.
FFS on values of X and Y
FFS on timeline requirement for multiplexing UCIs on PUSCH with A-CSI.
FFS how to handle one PUCCH overlap with multiple PUSCHs which satisfy timeline requirement.
FFS: how to handle HARQ-ACK for semi-static PDSCH.
FFS multiplexing rule when AN PUCCH resource with F1 overlaps with SR PUCCH resource with F0.
FFS: how to handle semi-statically configured PUCCH overlap with semi-statically configured PUCCH or PUSCH.
Note: The above proposal does not override the dropping rules defined for ACK/SR colliding with A-CSI-only on PUSCH without UL-SCH, or ACK/SR colliding with SP-CSI on PUSCH without UL-SCH.
Note: Consider how to handle PUCCH colliding with other UL channels in NR Rel. 15 June drop when URLLC is taking into account.

## Slide 4: Proposal (offline consensus)
When a configured CSI PUCCH resource overlaps with one or more configured SR PUCCH resources in a slot,
  The UE multiplexes all UCIs on the CSI PUCCH resource using the corresponding UCI multiplexing rules for the overlapping PUCCH resources with the same starting symbol.
  FFS: When one SR PUCCH resource overlaps with two non-overlapping CSI PUCCH resources

## Slide 5: Proposal
When HARQ-ACK/SR PUCCH resource determined by ARI and configured CSI PUCCH resources have the same starting symbols in a slot, if the UE is configured with only one PUCCH resource set and simultaneous transmission of HARQ-ACK/SR and CSI is enabled, select from one of the following alternatives:
  Alt 1: This is a mis-configuration. The UE is not expected to transmit the corresponding HARQ-ACK/SR and the CSI report in a PUCCH resource in that slot.
    Supportive companies: E//, Intel, OPPO, QC, HW, Samsung, Panasonic
  Alt 2: HARQ-ACK/SR and CSI are transmitted together by PUCCH resource for CSI
    Supportive companies: Nokia, MTK, Lenovo, Motorola, ZTE, CATT, DCM
  Alt 3: HARQ-ACK/SR is transmitted on the HARQ-ACK/SR PUCCH resource and CSI reporting is dropped in that slot.
    Supportive companies: LG, Vivo

## Slide 6: Proposal 1 (AN PUCCH Format 1)
Select one of the following two alternatives:
  Alt 1: If a HARQ-ACK transmission from a UE using PUCCH format 1 determined by ARI overlaps with K SR occasions each using PUCCH format 1, in case of negative SR, the HARQ-ACK is transmitted on the HARQ-ACK resource. In case of positive SR, the HARQ-ACK is transmitted on the SR resource corresponding to the positive SR.
    Supportive companies: Nokia, E//, CATT, LG, DCM, HW, Vivo, Panasonic, DCM
  Alt 2: PUCCH format 2 or 3 or 4 is used to carry L = 1 or 2 bits HARQ-ACK and K > 1 SR. That implies when a UE has K SRs configured in a same time position,
    For 1 or 2 bits HARQ-ACK, if K=0 or 1, ARI field in DCI indicates PUCCH format 0 or 1; otherwise, ARI field in DCI indicates PUCCH format 2 or 3 or 4.
    Supportive companies: Samsung, ZTE