## Slide 1: Way Forward on PUSCH Power Scaling in UL Power Control
Ericsson, Samsung, DOCOMO, CATT
3GPP TSG RAN WG1 #91
Busan, Korea, May 21st – 25th, 2018
Agenda item – 7.1.6.3
R1-18nnnnn

## Slide 2: Background
Section 7.1 of 38.213 describes PUSCH power scaling as:
  “For PUSCH, a UE first scales a linear value of the transmit power on UL BWP , as described in Subclause 12, of carrier of serving cell , with parameters as defined in Subclause 7.1.1, by the ratio of the number of antenna ports with a non-zero PUSCH transmission to the number of configured antenna ports for the transmission scheme. The resulting scaled power is then split equally across the antenna ports on which the non-zero PUSCH is transmitted. The UL BWP is the active UL BWP.”
For non-codebook and non- or partial-coherence codebook based transmission schemes, this means:
  UE transmits at most ½ or ¼ of its full Tx power for 2 or 4 ports
  Tx power is not divided equally among layers

## Slide 3: Proposal
Correct UL power control for PUSCH such that UEs configured for
  non-codebook based transmission,
  codebook based transmission with codebookSubset = ‘Non-Coherent’ or ‘partialAndNonCoherent’
is able to transmit with a total power independent of rank, allowing the UE to transmit at its maximum rated power.