## Slide 1: Summary #2 for Uplink Power Control for Supporting NN-DC
Agenda item: 7.2.13.1
Source: Apple Inc.
Title: Summary #2 for Uplink Power Control for Supporting NN-DC
Document for: Discussion
3GPP TSG-RAN WG1 Meeting #98
Prague, CZ, August 26th – 30th, 2019
R1-1909760

## Slide 2: Dynamic Power Sharing (1/4)
Power determination rule
Option 1: Reuse power determination of Rel-15 NR CA
  Symbol-by-symbol power determination for PUSCH transmission
  Supportive companies
    CATT
Option 1’: minimum guaranteed transmission power is configured on a per CG basis + CA power control.
  Supported:
Figure 1: Power determination for Rel-15 CA

## Slide 3: Dynamic Power Sharing (2/4)
Power determination rules
  Option 2: Introduce enhanced ‘look-ahead’ behavior
    When determining a total transmit power in a symbol of transmission occasion starting from t0 in CG1, the UE needs to consider all PDCCH(s) received before time that trigger an overlapping CG2 UL transmission.
    FFS on value of T_offset
Figure 2: Enhanced ‘look-ahead’ behavior
Figure 3: Potential phase discontinuity case

## Slide 4: Dynamic Power Sharing (3/4)
Power determination rules
  Option 3:
    When determining a total transmit power in a symbol of transmission occasion starting from t0 in CG1, the UE needs to consider all PDCCH(s) received before time that trigger an overlapping CG2 UL transmission.
      FFS on value
    Once the transmit power for a transmission is computed, UE will not re-calculate/re-adjust the transmit power based on upcoming transmission regardless of priority levels.
    Concerns
      Different priority rule applied for CA within a CG, compared to Rel-15 CA.
  Supportive companies:
    Motorola Mobility, Lenovo, Samsung, Nokia, Ericsson, ZTE, LG Electronics
Figure 4: Transmission power determination

## Slide 5: Dynamic Power Sharing (4/4)
On ‘look-ahead’ operation
  [Offline consensus]:
The prioritization rule for overlapped UL channels in case of power-limited is as follows
  Alt.1: MCG>SCG, and then apply Rel-15 rule for each CG.
  Alt.2: Reusing Rel-15 CA rule across CCs of CGs
  Alt.3: CG prioritization is determined by time pattern or dynamic indication, and then apply Rel-15 rule with potential update considering URLLC priority for each CG.
  Alt4: If P_MCG+P_SCG<P_total, no prioritization needed and UE limits its power according to P_MCG and P_SCG on MCG and SCG respectively. If P_MCG+P_SCG>=P_total then go with Alt1.
  Others?
  [Offline consensus]:

## Slide 6: Semi-static Power Sharing (1)
Alt.1: For the uplink transmission in MCG, the UE checks the semi-statically configured direction of the overlapping symbols of all serving cells of SCG and vice versa.
  If such overlapping with UL transmission on the SCG is possible (i.e. collides with semi-static ‘UL’ and ‘flexible’ symbols on all CCs of SCG), UE limits its actual maximum transmission power in MCG such that ;
  Otherwise (i.e. collides with only semi-static ‘DL’ symbols on all CCs of SCG), can be up to and can be up to .
    Alt.1-1: and are configured by RRC signaling.
    Alt.1-2: and are determined by RAN4 requirement.
Other alternatives?
[Offline consensus]