## Slide 1: Soft Buffer Allocation for Rel-10 Downlink
Huawei, HiSilicon, []
RAN1 WG1 #63, November 2010

## Slide 2: R1-105937 (CATT)
Solution 1: Separate soft buffer size management
  For the nc-th carrier, the soft buffer size for the transport block, NIR(nc), is
  Each CC is allocated the same size
  Concern:
    If the CCs have different capacity (Bandwidth, MIMO layers, etc), then the soft buffer should not be divided evenly

## Slide 3: R1-105937 (CATT)
Solution 2: Joint soft buffer size management
Each TB is allocated the same size
Concern:
  If MIMO mode of one CC is changed or one CC is activated/deactivated (configured/removed), soft buffer size of other CCs are affected
    This will disrupt the HARQ receiving process if the HARQ buffer has been filled with soft channel bits
  Different bandwidth and/or MIMO capability of the CCs may results in different maximum TB sizes of the CCs.

## Slide 4: Alternative 1
Modify Solution 1
Separate soft buffer size management, but each carrier may have different soft buffer size
Soft buffer size for the nc-th carrier, Nsoft(nc), is determined according to UE Category/capability parameters
Lmax(nc) : max number of DL MIMO layers on nc-th CC
Divide Nsoft(nc) between the TBs on nc-th CC according to Rel-8 equation

## Slide 5: Alternative 2
Discard the constraint of mother code rate 2/3 so that NIR(nc) is no longer necessary
Define the total soft buffer size in UE Category table such that it can hold all soft channel bits for all TBs
Parameter =8 if FDD; =15 if TDD
Pro:
  Turbo decoder performance 1/3 compared to 2/3, 1.2 dB better in QPSK+AWGN condition
Con:
  Soft buffer size is doubled for FDD, and 3.75 as large for TDD