## Slide 1: Way Forward on Radio-interface based synchronization
Huawei, HiSilicon, KDDI, NTT DOCOMO, CMCC, CATR, Research In Motion, ASUSTeK, Telefónica, IAESI, New Postcom, Telecom Italia, Deutsche Telekom, T-Mobile USA, Coolpad
3GPP TSG RAN WG1 #73 R1-132771
Fukuoka, Japan, May 20-24, 2013
Agenda item: 6.2.5.3

## Slide 2: Background
Non radio-interface based synchronization, such as GPS and IEEE 1588, is not always available or cost effective.
Beneficial to or required by many existing mechanisms or techniques under study in FDD and TDD:
  Interference coordination (e.g.(F)eICIC)/ Inter-eNB CoMP/ Carrier aggregation
  Efficient discovery of small cells
  Dual connectivity especially with single radio UL
  Interference cancellation and suppression at UE receiver
Strict requirement in TDD mode
  eNBs deployed by the same operator
  eNBs deployed by different operators in the same band

## Slide 3: Proposals
Synchronization for both TDD and FDD systems needs to be considered
In small cell SI, the study on inter-cell synchronization focuses on the following cases
  Synchronization between a small cell and the overlaid macro cell
  Synchronization between small cells in the same cluster
  Synchronization between small cell clusters
Further investigate the radio-interface based synchronization solutions (e.g. network listening, UE assisted synchronization)

## Slide 4: Proposals
Further study the solutions of radio-interface based synchronization on
  Achievable synchronization accuracy
  Resource overhead
  Applicability/compatibility with the ongoing studies
  Cost/complexity of eNBs and UEs
  Standard impacts
The achievable synchronization accuracy should be no worse than 3µs.
  The value is used to guide the study. It is not intended to impact the requirement discussion in RAN4.