## Slide 1: WF on Timing Synchronization of D2D Outside of Network Coverage
NEC, SAMSUNG
R1-134926
3GPP TSG RAN WG1 Meeting #74bis
Guangzhou, China, 7th – 11th October 2013 Agenda item: 7.2.8.1.1
Document for: Decision

## Slide 2: Background
To handle resource allocation and interference avoidance in broadcast communication, it is nice to have a common synchronization reference for UEs within the transmission range of each other.

## Slide 3: Background
Technically, there are two basic approaches for having a common synchronization reference:
  Centralised approach: in this approach, one D2D UE will take charge to provide D2DSS and potentially PD2DSCH for other D2D UE(s) within a local area defined by its transmission range:
    In this case, there is a heavy dependency on that D2D UE for providing the synchronization reference. If that D2D UE is removed or move away, there is a need for a re-selection of another D2D UE as a synchronization source.
    This approach is not easily scalable due to the limited transmission range and mobility of the synchronization source.
    There could be potentially multiple groups of D2D UEs each with a single synchronization source. In this case, D2D communication of D2D UEs with different synchronization reference is not easy.
  Distributed approach: In this approach, a non-particular D2D UE shall initiate D2DSS and potentially PD2DSCH for other D2D UEs within its transmission range to adopt a synchronization reference and each and every D2D UE(s) that has adopted that nominated synchronization reference could potentially transmit D2DSS and potentially PD2DSCH to provide and maintain synchronization reference within their transmission range.
    This approach is easily scalable at the expense of some initial convergence time.

## Slide 4: Proposal
It is beneficial that network-wide synchronization for timing synchronization of D2D outside of network coverage is supported:
  Network-wide synchronization means that D2D UEs with at least 2 hops distance among them have a common synchronization reference.
Network-wide synchronization is achieved through D2DSS and potentially PD2DSCH.
  Both centralised and distributed approach should be studied for timing synchronization of D2D outside of network coverage: Detailed design is FFS.