## Slide 1: WF on LAA functionalities
Huawei, HiSilicon, Intel, Kyocera, CATR, Ericsson, NTT DOCOMO, Nokia Networks, Nokia Corporation, CATT, Sharp, ZTE…
3GPP TSG RAN WG1 Meeting #79 R1-145379
San Francisco, USA, November 17 – 21, 2014
AI: 6.3.2.2

## Slide 2: Proposals for LAA DL design
DL LAA design should assume subframe boundary alignment across cells according to the Rel-12 CA timing relationships
  At least for LBE, some signal(s) can be transmitted between the time eNB is permitted to transmit and the start of data transmission
    This does not imply the data transmission can start only at the subframe boundary
    The duration of this signals(s) is part of the maximum transmission duration
    The content/function/duration of this signal is FFS
  This does not imply network synchronization
At least subframe or multi-subframe level on/off on the LAA Scell can be considered for efficient transmission on the unlicensed band

## Slide 3: Proposals
Support at least the following functionalities in addition to the current LAA TR on the unlicensed band
  RRM measurement
  AGC setting
  Coarse synchronization and fine frequency/time tracking
  CSI measurement, including channel and interference
Rel-12 DRS can be the starting point for at least RRM measurement

## Slide 4: Other regulatory requirements
The following functionalities are supported by legacy specifications and/or implementations
  Transmit Power Control as per regulatory requirement
  Dynamic frequency selection for radar avoidance at eNB in certain bands/regions
    FFS the necessity for enhancements to power control (not related to regulatory requirement)
    FFS if the DFS for radar avoidance is needed to be supported in the UE