## Slide 1: WF on UL simulation assumptions
Alcatel-Lucent, Alcatel-Lucent Shanghai Bell, Samsung, CMCC
3GPP TSG RAN WG1 #80 R1-150795
Athens, Greece, 9th – 13th February 2015
Agenda item: 7.2.4.1

## Slide 2: Proposal
Capture phase1 UL evaluation results on TR.
Parameters | Proposed Values
Channel model & BS antenna downtilt | Align with DL Phase 1 simulation assumptions
BS antenna element configurations | [M=8, N=4, P=2, Q=8]
BS antenna polarization | Cross-polarized
UE attachment | Align with downlink Phase 1 simulation assumptions
Carrier Frequency | 2GHz
Network sync | Synchronized
System bandwidth | 10MHz (50RBs)

## Slide 3: Proposal
Parameters | Proposed Values
UE distribution/speed/array orientation/antenna pattern | Aligned with DL phase 1 simulation assumptions
Wrapping method | Geographical distance based
Handover margin | 3dB
Traffic model | Mandatory: FTP, optional: full buffer
Scheduler | PF scheduler (considering single carrier property)
Receiver | Ideal/non-ideal channel estimation, both demodulation and sounding
 | Explicit intercell interference modelling
 | MMSE-IRC

## Slide 4: Proposal
Parameters | Proposed Values
Hybrid ARQ | Maximum 4 transmissions, CC
Transmission scheme | 1xMR SIMO (MR: the number of BS antenna ports)
Maximum UE TX power | 23dBm
Target BLER | 10%
Overhead | 2 SC-FDMA symbols per 1ms for the demodulation RS
 | 2 SC-FDMA symbols per 5ms for channel sounding RS
 | 8RBs for PUCCH
SRS configurations | 5ms of channel sounding RS period (infinite SRS capacity)
 | 4ms of channel sounding delay
Power control | P0=-80dBm, alpha=0.8
Metrics | Mean, 5%, 50% UPT
Number of Tx antenna at UE | 1 antenna

## Slide 5: Proposal
The companies are encouraged to bring the results for following antenna array configurations
  (M,N,P, Q)= (8,4, 2, 16/32/64)