## Slide 1: WF on buffer occupancy for UL+DL coexistence evaluations
Ericsson, Samsung
3GPP TSG RAN WG1 #80 R1-150857
Athens, Greece
9th – 13th February 2015
Agenda item: 7.2.3.2
Document for decision

## Slide 2: Background
Working assumptions:
A new metric, buffer occupancy is defined:
  Buffer occupancy is defined:
    Buffer occupancy of the i-th small cell/UE (Wi-Fi & LAA) = sum of the period of time during which the i-th small cell/UE has data to transmit including retransmissions (i.e., its queue is not empty) / total simulation time
    Average buffer occupancy: buffer occupancy averaged over the all small cells/UEs of the same operator
Agreements:
Confirm the working assumption of Buffer Occupancy (BO) as an output metric for at least DL only LAA evaluation
  The modifications of BO for uplink transmission is FFS
Report a ratio of mean served cell throughput and offered cell throughput

## Slide 3: Background
Buffer occupancy (BO) and the ratio of mean served cell throughput and offered cell throughput were agreed for DL-only coexistence evaluations.
Above metrics are needed to be clarified for the UL+DL coexistence evolutions.

## Slide 4: Proposal
Extend the agreement on the DL-only buffer occupancy for UL+DL coexistence evaluations.
For UL+DL coexistence evaluations the following should be reported:
  The ratio of mean served cell throughput and offered cell throughput on DL
  The ratio of mean served cell throughput and offered cell throughput on UL
  DL buffer occupancy (as defined in the working assumption)
  UL buffer occupancy (as defined in the working assumption)
Use max(DL BO, UL BO) as indicator of load in the system