## Slide 1
NEC, Ericsson, Alcatel-Lucent, Alcatel-Lucent Shanghai Bell, Nokia Networks, Nokia, Intel, Huawei, HiSi, ZTE, ETRI, Sierra Wireless, Fujistu, Qualcomm, Sony
  WF on Physical Channels for MTC
3GPP TSG RAN WG1 #80
Athens, Greece, February 9-13, 2015
Agenda item 7.2.1.2.1
R1-150911

## Slide 2: Background information
Agreement at RAN1#79:
  At least for unicast PDSCH transmission scheduled by ‘Physical downlink control channel for MTC’, cross-subframe scheduling is supported at least for Rel-13 UE supporting enhanced coverage

## Slide 3: Proposals
For enhanced coverage UEs:
  Repetition/bundling is supported for the ‘Physical downlink control channel for MTC’, PDSCH and ‘Physical uplink data channel’.
For Rel-13 low complexity MTC UEs:
  At least for unicast PDSCH transmission scheduled by ‘Physical downlink control channel for MTC’, cross-subframe scheduling is supported for normal coverage
    For a UE in normal coverage, it is allowed to have ‘Physical downlink control channel for MTC’ and un-associated PDSCH in the same subframe
    FFS: transmission of “Physical downlink control channel for MTC” and the associated PDSCH in the same subframe is supported