## Slide 1: WF on Energy Detection Threshold for LAA
Intel and Broadcom
R1-152290
3GPP TSG-RAN WG1 Meeting #80Bis
Belgrade, Serbia, 20th-24th April 2015
Document for: Decision
AI 7.2.4.2

## Slide 2: Background
Especially in the following evaluation assumptions:
  Indoor, Y=1 (# of unlicensed channel = 1)
  Closed loop MIMO (link/MCS/precoding adaptation) and short GI for Wi-Fi
  it is observed that:
  With -62 dBm LAA ED threshold, the UPT and VoIP outage performance of a Wi-Fi network degrades when another Wi-Fi network is replaced with an LAA network.
  With -82 dBm LAA ED threshold, the UPT and VoIP outage performance of a Wi-Fi network improves when another Wi-Fi network is replaced with an LAA network.
This is mainly due the fact that in addition to ED, preamble detection (CCA-CS) is performed by Wi-Fi nodes, of which performance threshold is assumed to be -82 dBm in the TR.

## Slide 3: Proposals
Proposal 1: The following observation from the coexistence evaluation results from some companies is explicitly captured in TR 36.889.
  Observation: With -62 dBm LAA ED threshold, LAA does not coexist well with Wi-Fi in some evaluation scenarios. To be more specific, with -62dBm LAA ED threshold, the UPT and VoIP outage performance of a Wi-Fi network degrades in some scenarios when another Wi-Fi network is replaced with an LAA network, while with -82dBm LAA ED threshold, the UPT and VoIP outage performance of the Wi-Fi network improves in the same scenarios when the Wi-Fi network coexists with the LAA network.
Proposal 2: LAA should support a mechanism to adaptively lower the ED threshold from a specified upper bound, e.g., -62dBm.
  FFS: the specified upper bound
  FFS: the value of the ED threshold actually used (active threshold)
  FFS: Adaptation mechanism