## Slide 1: Way forward on Resource Allocation for PDSCH
NTT DOCOMO, Alcatel-Lucent, Alcatel-Lucent Shanghai Bell, Ericsson, InterDigital, Lenovo, Nokia Neworks, NEC, Samsung, KDDI, MediaTek, Intel, LG Electronics, Huawei, HiSilicon
3GPP TSG RAN WG1 Meeting #81
Fukuoka, Japan, May 20 – 29, 2015
Agenda Item: 6.2.1.1
R1-153680

## Slide 2: Proposal
Confirm the following working assumption at RAN1#80bis meeting
Working assumption:
For Rel-13 low complexity UEs in normal [FFS: small enhanced] coverage, under cross-subframe scheduling (k > 0),
  Case 1:
    For unicast PDSCH, DCI indicates one of narrow-band and further indicate resource allocation within narrow-band
      This doesn’t preclude predefined frequency hopping
      FFS: Details on resource allocation field in DCI
    CSI measurements can be restricted to a subset of the available narrow-bands
      FFS: details
  FFS: whether and/or how to define a case (Case 2) that UE can assume PDSCH is always scheduled from the same narrowband where the corresponding M-PDCCH has been transmitted.

## Slide 3: Background for k value
The following was agreed at RAN1#80bis meeting
Value of k is:
  Option 1: k is fixed
    Option 1-A: k=1 or 2, where PDSCH is allowed to use a different narrowband from the associated EPDCCH
      RAN1 will select a single value of k after receiving RAN4 input on retuning time
    Option 1-B: k=1, where PDSCH always use the same narrowband location as the associated EPDCCH
    FFS for the subframe n+k not allowed for PDSCH (e.g. PMCH, TDD, HD-FDD)
  Option 2: k is variable
  When not operating coverage enhancement, Option 1 is used when cross-subframe scheduling is used

## Slide 4: Proposal
Value of k in Case 1 is:
  k>=2
    RAN1 will select a single fixed value of k after receiving RAN4 input on retuning time
    Company should investigate impact on UE complexity of M-PDCCH decoding (R1-153082).
    When k > 2, RTT may need to be modified.
FFS: Value of k in Case 2 is:
  k=1
FFS for the subframe n+k not allowed for PDSCH (e.g. PMCH, TDD, HD-FDD)
This overrides the previous agreement on the previous slide.