## Slide 1: WF on Paging
Alcatel-Lucent, Nokia Networks, Ericsson
R1-15XXXX
3GPP TSG RAN WG1 Meeting #82bis
Malmö, Sweden, 5th – 9th October 2015
Agenda item 7.2.1.8

## Slide 2: Background
RAN1#82 Agreements
  Confirm the working assumption to use M-PDCCH scheduled PDSCH carrying paging record(s)
  One or more narrowbands can be configured by eNB for paging
    A UE monitors a paging occasion in one of the configured narrowbands in the subframe based on at least UE ID at least for paging record(s)
  On indicators for system information update, ETWS, and CMAS:
    Option A: Transmit in M-PDCCH
    Option B: Transmit in PDSCH
    FFS if the paging occasion for SI update, ETWS, and/or CMAS is a cell common or not
    FFS additional information (e.g. CFI, TDD configuration) in the associated DCI or paging message
  The M-PDCCH search space for paging includes M-PDCCH candidate(s) with the highest CE level configured in the cell
    Note: the ‘CE level’ can be replaced by a proper terminology later if needed

## Slide 3: Proposal
  Indicators for system information update, ETWS, and CMAS are transmitted in M-PDCCH (option A)