## Slide 1: Way forward on observations of link-level simulation results
MediaTek, CHTTL, ZTE
3GPP TSG RAN WG1 #82bis
Malmo, Sweden, 5th – 9th October 2015
Agenda item 7.2.7.2
R1-156233

## Slide 2: Background
  The observations are drawn from the following link-level simulation results
    R1-155700 (MediaTek), R1-155324 (Intel), R1-155408 (LG), R1-155640 (Huawei), R1-153822 (Alcatel-lucent), R1-154537 (NTT DoCoMo), R1-154058 (ZTE)
  Assumptions in the simulation results
    2x2 antenna configuration
    Same transmission scheme of either TM4 or TM9
    Same RI/PMI
    Same resource allocation for MUST users
    Same PDSCH RE mapping for MUST users
    The following assistance information is assumed known
      Transmission power or bit rate ratio of co-scheduled users
      Modulation order of co-scheduled users
      DMRS information if TM9 is applied
      Existence of MUST interference

## Slide 3: Observations (1/2)
  For the MUST-near user:
    In MUST category 1, R-ML/ML receiver can achieve similar link-level performance as CWIC receiver when the MUST-far user uses QPSK and holds high transmission power ratio
    In MUST category 2, R-ML/ML receiver can achieve similar link-level performance as CWIC receiver when MUST-far user uses QPSK
    In MUST category 3, R-ML/ML receiver can achieve similar link-level performance as CWIC receiver when MUST-far user uses significant bit(s) in the label bits of a modulation symbol
    For other cases, there may be noticeable performance degradation of R-ML/ML receiver, compared to CWIC receiver

## Slide 4: Observations (2/2)
For the MUST-far user:
  In MUST category 1, MMSE-IRC receiver can achieve similar link-level performance as R-ML/ML receiver when the MUST-far user uses QPSK
  In MUST category 2, MMSE-IRC receiver can achieve similar link-level performance as R-ML/ML receiver
  In MUST category 3, MMSE-IRC receiver can achieve similar link-level performance as R-ML/ML receiver
  For other cases, there may be noticeable performance degradation of MMSE-IRC receiver, compared to R-ML/ML receiver