## Slide 1: WF on Paging for eMTC and UE in CE
InterDigital, Sony, Intel, Sierra Wireless, NTT Docomo, Qualcomm, Alcatel-Lucent, Alcatel-Lucent Shanghai-Bell, MediaTek, Nokia, KDDI, NEC, Huawei, HiSilicon, Ericsson, LG Electronics, ZTE
R1-156286
3GPP TSG RAN WG1 Meeting #82bis
Malmö, Sweden, 5th – 9th October 2015
Agenda item 7.2.1.8

## Slide 2: Background
RAN1#82 Agreements
  Confirm the working assumption to use M-PDCCH scheduled PDSCH carrying paging record(s)
  One or more narrowbands can be configured by eNB for paging
    A UE monitors a paging occasion in one of the configured narrowbands in the subframe based on at least UE ID at least for paging record(s)
  On indicators for system information update, ETWS, and CMAS:
    Option A: Transmit in M-PDCCH
    Option B: Transmit in PDSCH
    FFS if the paging occasion for SI update, ETWS, and/or CMAS is a cell common or not
    FFS additional information (e.g. CFI, TDD configuration) in the associated DCI or paging message
  The M-PDCCH search space for paging includes M-PDCCH candidate(s) with the highest CE level configured in the cell
    Note: the ‘CE level’ can be replaced by a proper terminology later if needed

## Slide 3: Proposal
  One alternative is selected between Alt-1 and Alt-2
  Alt-1: in each PO, an RRC idle UE monitors two DCI types (Type-A and Type-B)
    Type-A DCI with P-RNTI includes scheduling information of PDSCH which carries paging record(s) only or paging record(s) together with system information update, CMAS, and/or ETWS.
    Type-B DCI with a new RNTI includes system information update, CMAS, and ETWS without scheduling information of PDSCH.
    Type-A DCI and Type-B DCI are the same size
    A UE may assume that a single DCI type is transmitted in a PO.
  Alt-2: in each PO, an RRC idle UE monitors one DCI type
    The DCI include an indicator (e.g. S_flag)
    An indicator (e.g. S_flag) used in the DCI with P-RNTI for paging
      If S_flag=TRUE, the rest of DCI bits carries scheduling information of PDSCH for paging message
      If S_flag=FALSE, the rest of DCI bits carries system information update, ETWS, and CMAS without scheduling information of PDSCH