## Slide 1: WF on reducing the number of blind decodes
Panasonic, Samsung, LG, CATT, Qualcomm
R1-156307
3GPP TSG RAN WG1 #82bis
Malmo, Sweden, 5th – 9th October 2015
Agenda item 7.2.2.2

## Slide 2: Background
Current (E)PDCCH search space is designed to avoid (E)PDCCH blocking among UEs
In case of small cell scenario, the number of UEs to be scheduled on one cell is small. (E)PDCCH blocking probability among UEs is small
  Current number of (E)PDCCH candidates is not necessary
For cross carrier scheduling, the search spaces are determined by following equation:
  where
nCI is the carrier index

## Slide 3: Proposals
nCI can be configured by higher layer signalling by eNB, so that the search space of different carriers of the UE can completely overlap
Other methods to reduce the number of blind decodings are not precluded
Reducing the number of blind decodes by configurable further reduction of the search space on some carriers is not precluded

## Slide 4: Benefits
The number of blind decodings is reduced
There is no impact on (E)PDCCH blocking