## Slide 1: 3GPP TSG RAN WG1 Meeting #82bis R1- 156328 Malmo, Sweden, October 5-9, 2015 Agenda item 7.2.1.9
WF on section 7.2.1.9
[Huawei], [HiSilicon], [Ericsson],[MediaTek],……

## Slide 2: Proposals on non-simultaneous reception Huawei, HiSilicon, MediaTek, NTT DOCOMO, CATT, Sony, [Intel], [ALU]
For UEs operating CE, define at least the following priority rules:
For UE acquiring the indication of system information update, SIB has highest priority.
Else
    During a RAR window, M-PDCCH for RAR has highest priority
      Subsequent reception of RAR has highest priority in relevant subframes
    In a paging occasion not colliding RAR window, M-PDCCH for paging has highest priority (if UE is RRC_IDLE).
      Subsequent reception of paging has highest priority in relevant subframes

## Slide 3: Proposals on SRS transmission Ericsson, Qualcomm, Sequans, Verizon, Panasonic, Alcatel-Lucent, Alcatel-Lucent Shanghai Bell, Samsung, Nokia Networks, Sony, Intel, [LGE]
At least for medium-to-large CE case, LC/CE UE does not support SRS transmission
The following fields in cell-specific SRS configuration are broadcast to LC/CE UE:
  srs-BandwidthConfig
  srs-SubframeConfig
  ackNackSRS-SimultaneousTransmission
For PUSCH transmission in cell-specific SRS subframe with R=1, the same UE behavior with Rel-12
For PUCCH transmission in cell-specific SRS subframe with R=1, shortened PUCCH is always used
FFS: PUSCH and PUCCH transmission in cell-specific SRS subframe when R > 1

## Slide 4: Proposals on cell identification MediaTek,[Huawei],[HiSilicon]
Send LS to RAN4 for further checking the feasibility of the relaxed requirement for cell identification about PSS/SSS detection.