## Slide 1: WF on CFI for MTC
Ericsson, LG, Intel, Samsung, Qualcomm, Sony, NTT DoCoMo, Nokia Networks, Sierra Wireless, MediaTek, Panasonic, NEC, ZTE
R1-156341
3GPP TSG RAN WG1 Meeting #82bis
Malmö, Sweden, 5th - 9th October 2015
Agenda item 7.2.1.6

## Slide 2: Background (1)
Working Assumption from RAN1#80:
For subframes containing PDSCH carrying MTC SIB1, the starting OFDM symbol of MTC SIB1 reception is a fixed value predefined in the specification
  The fixed value is equal to the maximum CFI value for the given system configuration (TDD/FDD, system bandwidth)
  Here “MTC SIB1” refers to the first SIB that carries configuration information for the low-complexity/coverage-enhancement UE
  FFS: Handling of duration of DwPTS for TDD
For "Physical downlink control channel for MTC" and other PDSCH, the starting OFDM symbol is broadcast to all low-complexity/coverage-enhancement UEs in a cell via a shared higher layer parameter in MTC SIB1.
  The higher layer parameter is a 2-bit field, indicating starting OFDM symbol  {1,2,3} for N_RB^DL >10 , and  {2,3,4} for N_RB^DL 10
  As in existing system, the starting OFDM symbol for subframe 1 and 6 for TDD is maximum 2
  FFS if starting OFDM symbol can be 0
FFS: MBSFN subframe handling
Agreements:
Confirm WA unless MIB is agreed to indicate starting OFDM symbol for low-complexity UEs in coverage-enhancement

## Slide 3: Background (2)
R1-155058, “LS on system information broadcast, random access, and paging for Rel-13 LC/CE UEs” from RAN2
  Agreements (SIB)
  The list of aspects provided under proposal 1 in the email discussion on SIB contents (R2-153277) is agreed with some exceptions:
    …
    1.25: This is only a working assumption subject to decision by RAN1.
1.25 [Recommendation 17] To define the following new fields or information:
  Control Format Indicator (CFI) is defined to indicate the size of legacy PDCCH region e.g. as 2-bit indicator (i.e. for one, two, or three OFDM symbols and one spare value)

## Slide 4: Proposal
Confirm the Working Assumption with revised description of the same:
  For subframes containing PDSCH carrying SIB1bis, the starting OFDM symbol of SIB1bis reception is a fixed value predefined in the specification
    The fixed value is equal to the maximum CFI value for the given system configuration (TDD/FDD, system bandwidth)
    FFS: Handling of duration of DwPTS for TDD
  For M-PDCCH and other PDSCH, the starting OFDM symbol is broadcast to all low-complexity/coverage-enhancement UEs in a cell via a shared higher layer parameter in SIB1bis
    The higher layer parameter is a 2-bit field, indicating starting OFDM symbol  {1,2,3} for N_RB^DL >10 , and  {2,3,4} for N_RB^DL 10
    As in existing system, the starting OFDM symbol for subframe 1 and 6 for TDD is maximum 2
  FFS: MBSFN subframe handling