## Slide 1: WF on UE-reported RSSI
Samsung, Intel, …
3GPP TSG RAN WG1 #83 R1-157621
Anaheim, USA
15th – 22nd November 2015
Agenda item: 6.2.3.2
Document for decision

## Slide 2: Background
Agreements in RAN2#91bis:
  1: Average RSSI over a L3 averaging window is a mean of all measurements from L1.
  1a Channel occupancy is calculated over the same L3 averaging window.
  1b UE always reports both Average RSSI and Channel occupancy together.
  2 Timing configuration for average RSSI measurement and channel occupancy are the same.
  FFS Whether the channel occupancy is calculated on the same L1 samples used for average RSSI or whether more frequent L1 samples are used.
Discussion point:
L1 provides a single RSSI sample value for every “L1 averaging duration of UE-reported RSSI measurement” in a “Measurement duration of UE-reported RSSI measurement”
How many L1 samples are utilized for constructing the metrics depends on how the L3 filtering window is applied across multiple measurement durations

## Slide 3: Proposal
The relationship between L1 samples and a L3 window for constructing average RSSI and channel occupancy is as follows:
  For Average RSSI, L3 filtering can be applied and a single value is provided based on an average of all L1 averaging durations in every measurement duration within the L3 window
  For Channel Occupancy, no L3 filtering is applied, i.e. each L1 averaging duration is individually compared against the configured threshold to compute a single channel occupancy percentage over the multiple measurement durations within the window
    Metric definition: % of L1 averaging durations > RSSI_Thresh

## Slide 4: Example
L1 averaging duration = 1 OFDM symbol, UE-reported RSSI measurement duration = 70