## Slide 1: WF on the possible use of FD-MIMO with LAA
Mediatek, Broadcom, Cablelabs
3GPP TSG RAN WG1 #83 R1-157658
Anaheim, USA, 15th - 22th November 2015
Agenda item: 6.2.3.1
Document for decision

## Slide 2: Background Agreements from RAN1 #82
Agreements:
RAN1 shall identify adaptation rules for LAA to adaptively lower the maximum energy detection threshold to ensure co-existence with other RATs including Wi-Fi and good performance of LAA
  Technologies that ensure co-existence with other RATs including Wi-Fi, using alternative means not requiring lowering of the maximum energy detection threshold, are not precluded.
At least the following shall be considered in defining the adaptation rules of the maximum energy detection threshold:
  Antenna gain and number of transmit antennas
  Coexistence with LAA in absence of other RATs including Wi-Fi
  The maximum rated EIRP of the LAA transmission point within unlicensed band
  The maximum EIRP within the transmission burst following the LBT procedure
  The transmission bandwidth
  Measured ambient noise floor
  Deployment scenario: Indoor, outdoor
  Estimated Load on the operating channel
  Feasibility of the co-existence test
  Single global solution
In regions and bands/sub-bands without regulations, define an upper bound for the maximum energy detection threshold taking into consideration
  May be based on bandwidth and presence of other RATs

## Slide 3: Background
In RAN1 #82bis, in the context of CSI signaling discussion, whether FD-MIMO related signaling can be used in LAA was discussed.
The use of FD-MIMO can worsen the hidden node problem.
Typically RTS/CTS is used to handle the hidden node problem.
  There won’t be a RTS/CTS like solution in Rel-13
Analysis is provided in the contribution embedded below.

## Slide 4: Proposal
In Rel-13, FD-MIMO cannot be operated with LAA.