## Slide 1: WF on Forward Compatibility
Huawei, HiSilicon
3GPP TSG RAN WG1 #84bis R1-163555
Busan, Korea
11th – 15th April 2016
Agenda item: 8.1.2
Document for decision

## Slide 2: Observations
For forward compatibility and for compatibility of different features within each release, the following observations are made:
  Support of Coexistence over a single continuous block of spectrum
    NR and other 3GPP RAT (e.g. LTE, NB-IoT)
    different NR numerologies
    different services
  Support of multiple services (in any phase/release)
    services using future designs (e.g. waveform, frame structure, multiple access, etc)
    services using the same OFDM-based waveform with different numerology
  Support of accommodating new technical features
    seamlessly integrate new device categories
    enable UEs that do not support the full system BW (e.g. low-cost MTC)

## Slide 3: Proposal 2
Phase 1 and later phases of NR should be designed with the following principles to ensure forward compatibility and compatibility of different features:
  Support of blank resources in time/frequency
  waveform with lower emissions outside the useful subbands compared to CP-OFDM without windowing and filtering
  Strive for
    Minimizing the amount of signals/resources that needs to be transmitted irrespective of incoming traffic
    Maximizing the amount of resources that can be flexibly utilized without causing backward compatibility issues in the future
    Minimizing transmission of (always-on) wideband signals and channels
Continued on next page

## Slide 4: Proposal 3
  Flexible configuration of signals, channels and resources
    Strive to avoid short periodicity of always-on periodic signals and channels
    Rely more on dynamically configured quantities
  Physical layer functionalities (signals, channels, signaling) should be confined within its flexibly-configured time/frequency resource (for control, data, reference signals)
  Rely more on UE-specific quantities