## Slide 1: WF on Signaling of UL Channel Access Parameters
Ericsson, Huawei, HiSilicon
R1-16xxxx
3GPP TSG RAN WG1 Meeting #84bis
Busan, Korea, April 11–15, 2016
Agenda item 7.3.1.5

## Slide 2: Proposal
The LAA UL LBT parameters can be signaled dynamically to UEs.
The signaling of UL LBT parameters can include the following information:
  LBT option to use
    Option 1: LBT based on Category 4
    Option 2: LBT in a gap of duration 25 µs
    Option 3: No LBT with a gap of 16 µs
      Note: Option 3 is targeted for transmissions with a gap of fixed duration of 16 µs between the DL and UL transmission.
  Change of LBT option
  Start time of transmission
    Note: This information does not necessarily requiring explicit signalling.
FFS on other LBT parameters if needed
FFS whether/how in the absence of new UL LBT parameters, UE can assume the previously signalled LBT parameters.
Note: It is the eNB’s responsibility to ensure that channel access requirements are fulfilled in case of option 2 and 3.