## Slide 1: WF on link level models for MIMO simulations
TSG-RAN WG1 #85 R1-165402
Nanjing, China, May 23 – 27, 2016
Source: Ericsson, AT&T, ETRI, Huawei, HiSilicon, Intel, KT Corporation, Nokia, NTT DOCOMO, Qualcomm, Samsung
Agenda Item: 7.2.4
Document for: Discussion, Decision

## Slide 2: Background
TDLs and CDLs for NLOS and LOS have been agreed in R1-163476 and R1-163491
  The link level models can be scaled in delay to represent different levels of time dispersion
  A filtering approach to go from CDL to TDL has been agreed in R1-163490 – this implicitly captures the effect on delay spread from beamforming
In the NR study item, evaluations with MIMO are being discussed
The multiantenna aspects of the link level models have not been paid much attention
CDLs with fixed DoAs are not very suitable for MIMO simulations for several reasons;
  The PMI statistics can become very biased
  A fixed precoder may perform better than open-loop and on par with closed-loop or reciprocity BF
  A CDL only represents a single channel realization
  All link simulations would require detailed antenna array assumptions to be made and agreed on

## Slide 3: MIMO link level simulations
Two approaches:
  1. Make the CDLs more general by introducing angular translation and scaling
    Translation: mean angle can be changed by
    Scaling: angular spread can be changed
      Typical angular spreads for different scenarios can be obtained from the system-level model
    Can be applied to some or all of azimuth and zenith AODs and AOAs
    Note: The angles may need to be wrapped around to be within 0-360 degrees
  2. Use TDLs in combination with correlation matrices
    The approach from 36.101/36.104 can be reused
    Some guidance on selecting correlation parameters a,b,g needed (36.10x values are not necessarily typical)
    Typical correlation parameters can be derived:
      from scaled CDLs according to approach 1 + antenna array assumptions
      from system-level model + antenna array assumptions
      by selecting corner cases, e.g. uncorrelated, highly correlated etc.
is the tabulated CDL angle
is the rms angular spread of the tabulated CDL
is the translation angle
is the desired rms angular spread
is the resulting cluster angle

## Slide 4: Proposals
Proposal 1: Introduce angular translation and angular spread scaling to the agreed CDLs
  A method for scaling and translation to be described in the TR
  Guidlines on selecting scaling and translation parameters to be captured in the TR
    Note: This can be done with a similar approach as the delay scaling
Proposal 2: Introduce correlation matrices to be used together with the TDLs
  The correlation matrix construction method from 36.101/36.104 can be reused
  Guidlines on selecting correlation parameters to be captured in the TR
  Note: This approach can be applied to TDLs derived from spatially filtered CDLs according to R1-163490 to emulate hybrid BF