## Slide 1: WF on transmission and triggering SRS without PUSCH
Huawei, HiSilicon, Qualcomm, Samsung, ZTE, Intel, ITL, [Nokia, ALU, Intel, Ericsson]…
3GPP TSG RAN WG1 #85 R1-165573
Nanjing, China
23rd – 27th May 2016
Agenda item: 6.2.1.2
Document for decision

## Slide 2: background
Agreements in RAN1 84bis
A-periodic SRS without PUSCH is supported at least in DL ending partial subframes in Rel-14 eLAA WI
  FFS the case of UL subframes
SRS, if present in a UL subframe, is transmitted at the end of the subframe
Aperiodic SRS without PUSCH can be triggered by dynamic signaling at least via DL grants
  UE is configured by RRC one or more sets of SRS parameters
    The configuration details are FFS
  FFS other possible triggering mechanisms, e.g.:
    Group DCI
    UE-specific DCI
    One or several of the above options may apply

## Slide 3: Proposal
When SRS without PUSCH is transmitted in DL ending partial subframes,
  UE transmits SRS in symbol 13
    FFS in other symbols

## Slide 4: Proposal
If the aperiodic SRS without PUSCH is triggered via DL grants, following are needed
    Subframe timing k . This field will be omitted if subframe timing is predefined.
    FFS SRS LBT type, e.g., cat.2/cat.4
      Depends on whether or not the UE knows of the MCOT

## Slide 5: Proposal
Common/Group DCI can be used to trigger a-SRS without PUSCH for a group of UEs on the LAA Scell
The triggering signaling includes the following fields
    Subframe timing k. This field will be omitted if subframe timing is predefined.
    FFS SRS LBT type, e.g., cat.2/cat.4
      Depends on whether or not the UE knows of the MCOT
    CIF, if cross carrier indication from PCell is supported
    UE-specific field: trigger or not
The group ID/RNTI is configured to the UE via RRC signaling

## Slide 6: Appendix
Example of group DCI (extension of 3/3A)
  Group RNTI
  following information for the group
 | Information
CIF | if cross carrier indication from PCell is supported
Subframe timing “k” | If subframe timing is predefined, this field will be omitted.
SRS LBT type(1 bit) | Cat.2/cat.4
UE_1 specific field (1 bits) | Trigger or not
UE_2 specific field(1 bits) | 
… | 
UE_k specific field(1 bits) |