## Slide 1: WF on Time Reference for Ack/Nack Transmission
Ericsson, Nokia, Alcatel-Lucent Shanghai Bell, Sony, Verizon, AT&T, LG, Sierra Wireless
R1-165651
3GPP TSG RAN WG1 meeting #84bis
Nanjing, China,23rd-27th May, 2016
Agenda item 6.1.6

## Slide 2: Background
Two Alternatives are under discussion for the time reference point of UL A/N transmission
Alt 1: Baseline time point for time domain allocation:
  A/N transmission is relative to the first time reference point which is at least 12 ms later than the end of NPDSCH
  The period of the time reference point is fixed to [2]ms.
    The start of the period is from (SFN#0, subframe#0).
Alt. 2: A/N transmission delay is relative to the end of the corresponding NPDSCH transmission plus 12ms.

## Slide 3: Current RAN1 agreements:
The start of UL A/N transmission is >=12ms later than the end of the corresponding NB-PDSCH transmission
The size of resource unit for A/N transmission is 2 msec for 15 kHz single tone and 8 msec for 3.75 kHz single tone transmission
Fixed baseline subcarrier, and
  3.75kHz: 3 bits for frequency allocation, 1 bit for time allocation
    Starts from subcarrier 45, and offset grows negatively
      Offset values are {0, -1, -2, -3, -4, -5, -6, -7}
    Time offset is 0,1 x 8ms
  15kHz: 2 bits for frequency allocation, 2 bit for time allocation
    Starts from subcarrier zero, and offset grows positively
      Offset values are {0, 1, 2, 3}
    Time offset is 0,1,2,3 x 2ms

## Slide 4: Observations
Increment of NPDSCH transmission latency and impact on UE data rate are observed in R1-164100 due to the ACK/NACK timing alignment.
Fragmented downlink subframes due to the presence of invalid DL subframes make it very difficult to align the ACK/NACK timing (discussed in R1-165000).
The current RAN1 agreement works well without the ACK/NACK timing alignment.
If need, ACK/NACK alignment can be achieved by eNB scheduling based on the current RAN1 agreement without introducing additional reference point (discussed in R1-165000).

## Slide 5: Proposal
Uplink A/N transmission delay is relative to the end of the corresponding NPDSCH transmission plus 12ms.
  That is: Alt 2; Do not introduce the time reference grid to existing agreements