## Slide 1: WF on CCA Detection Threshold for eLAA
CableLabs, Broadcom, Orange, Marvell
3GPP TSG RAN WG1 #85 R1-165688
Nanjing, China
23rd – 27th May 2016
Agenda item: 6.2.1
Document for decision

## Slide 2: Background
Field measurements across a large number of deployed Wi-Fi infrastructure showed a median RSSI of -85 dBm for UL [1], and -80 dBm for DL [4].
CCA set at -72 dBm ignores 85% of UL Wi-Fi devices.
For signal levels around -85 dBm, a reliable reception is feasible since the related noise floor is around -94 dBm.
The recent LS from IEEE WG, requested to consider ED threshold values lower than -72 dBm [3], [5]
Comparing user RSSI distribution from 3GPP evaluation methodology (EVM) and field data showed that EVM captures a specific interference scenario limited to RSSI levels higher than -82dBm and mostly above -72dBm with a median around -50 dBm [2].

## Slide 3: Proposal
The evaluation methodology (EVM) shall be updated to include deployment scenarios representing RSSI distributions better aligned with real deployments.
The CCA threshold in eLAA shall be below -72 dBm.
  FFS: detection threshold level based on #1
  FFS: actual detection mechanism(s) (e.g. energy detection)

## Slide 4: References
[1] R1-162982, “Energy Detection Threshold for UL LAA Channel Access Mechanism” by CableLabs, 3GPP RAN1 Meeting 84b, Busan, Korea, April 11-15, 2016.
[2] “Consolidation Simulation and Field Based Data towards Fair Coexistence Tests” by Broadcom, WFA WiFi/LTE-U Coexistence Workshop, San Jose, CA, April 26th, 2016.
[3] R1-163375, “Liaison Statement to 3GPP from IEEE 802 LMSC”, 3GPP RAN1 Meeting, 3GPP RAN1 Meeting 84b, Busan, Korea, April 11-15, 2016.
[4] R4-164432, “Testing Level of Received Signal for LAA Channel Access Mechanism” by CableLabs, 3GPP RAN4 Meeting 79, Nanjing, China, May 23-27, 2016.
[5] R1-164114, “LS regarding 3GPP LTE based technologies operating in the unlicensed bands” (Counsel of Mayor of City of New York), May2, 2016