## Slide 1: WF on TDD latency reduction
Huawei, HiSilicon, CMCC, Nokia, ASB, Panasonic, Ericsson, ZTE
3GPP TSG RAN WG1 #85 R1-165892
Nanjing, China, May 23 - 28, 2016
Agenda item: 6.2.10.1

## Slide 2: Background
Working assumption:
  It is recommended to support a design that is based on 2-symbol sTTI and 1-slot sTTI for sPDSCH/sPDCCH
  It is recommended to support a design that is based on 2-symbol sTTI, 4-symbol sTTI, and 1-slot sTTI for sPUCCH/sPUSCH
    During the WI phase, down-selection is not precluded
  The working assumption is automatically confirmed by the end of Thursday if no significant issues are found
  Note: the supported sTTI lengths are not intended to impact discussion on additional subframe types in TDD.

## Slide 3: Proposals
Confirm the working assumption for FDD
Take the following agreement for FS2 TDD
  It is recommended to support a design that is based on 1-slot sTTI for sPDSCH/sPDCCH/sPUSCH/sPUCCH for FS2 TDD in Rel-14
  It is recommended to consider other sTTI duration(s) and additional DL-UL switching points for FS2 TDD latency reduction in Rel-15