## Slide 1: WF on Channel Coding Selection
Qualcomm Incorporated, Samsung, Nokia, ZTE, MediaTek
3GPP TSG RAN WG1 #86 R1-166376
Gothenburg, Sweden, Aug 22 - 26, 2016
Agenda item: 8.1.4.1

## Slide 2: Background
Agreements in RAN#84b
  Candidates for 5G new RAT data transmission are identified as the following
    LDPC code
    Polar code
    Convolutional code (LTE and/or enhanced convolutional coding)
    Turbo code (LTE and/or enhanced turbo coding)
    Note: It is RAN1 common understanding that combination of above codes is not precluded
    Note: Outer erasure code is not precluded
eMBB | mMTC | URLLC
 | Convolutional codes | Convolutional codes
LDPC | LDPC | LDPC
Polar | Polar | Polar
Turbo | Turbo | Turbo
Agreements in RAN#85 on code comparison
  Observations on AWGN performance for large information block length
  WF on channel coding simulation data sharing
  WF on further study of complexity of channel code

## Slide 3: Background Work Plan
RAN1#85 (May 2016)
  Continue discussing candidate channel coding and modulation
    Narrow down the candidate channel coding modulation
RAN1#86 (August 2016)
  Continue discussing candidate channel coding and modulation
    Make initial decisions on the channel coding and modulation
      Channel coding and modulation may be different depending on usage scenario

## Slide 4: Way Forward
LDPC should be selected for eMBB data channel to provide performance and implementation advantages at high rate and large blocklength