## Slide 1
3GPP TSG RAN WG1 Meeting #86 R1-167951 Gothenburg, Sweden, 22nd - 26th Aug 2016
Agenda item: 8.1.5
WF on Digital Subsystem with Hybrid Beamforming
Nokia, ASB,…

## Slide 2: Background, the problem
In previous RAN1 meetings a common assumption has been that hybrid transceiver architecture would be a typical choice for >6GHz NR deployments at BS (and at UE as well) because of
  Very wide system bandwidths, from hundreds of MHz up to few GHz available at higher carrier frequencies, lead to low/moderate number (e.g. 2-8) of high accuracy full bandwidth transceiver units (TXRUs) because of power consumption and cost
Characteristics for hybrid beamforming is operating with limited number of RF beams in parallel that can cover only portion of the cell coverage at a time

## Slide 3: Background, the problem
For instance in uplink operation, reception of scheduling request signals, random access channel and sounding reference signals from UEs around the sector, multiple time slots are needed (i.e. beam sweeping)
  The more narrow the beams, the less UEs can share the same beam and thus given the low number of available high accuracy and large bandwidth TXRUs, the multiplexing capacity of UL signals will be limited by the number of TXRUs
Operation using hybrid beamforming system especially with high number of active UEs in the cell introduces deteriorations compared to full digital system
  Physical layer latency and uplink control channel capacity
    For instance, scheduling latency increases with decreasing number of parallel beams with fixed scheduling request (SR) resource overhead in the system (achievable Tx periodicity per UE gets lower)

## Slide 4: Background, Potential solution (1/2)
Potential solution to improve hybrid Rx operation could be an implementation of a cost effective digital RX subsystem along with the main hybrid RX system
The digital RX subsystem could be used for reception of certain uplink control channels and small payload data transmissions in parallel with the main hybrid RX
The cost effective digital subsystem could be build for instance using high number of narrowband RXRUs or low accuracy RXRUs, or a combination of both.
Considering the narrowband option more promising, NR supporting control channels with bandwidths << system bandwidth, it would be attractive option to implement a subsystem with high number of narrowband RXRUs to build a “full digital” receiver being able to process UL signals from the whole sector at once with high enough array gain and high DoA resolution capabilities
Benefits include:
  Physical layer latency reduction
  Capacity increase in terms of number of active UEs
  Reduced system overhead

## Slide 5: Background, Potential solution (2/2)
TXRU
TXRU
TXRU
TXRU
TXRU
TXRU
TXRU
TXRU
TXRU
Wide BW (hundreds of MHz to few GHz), high accuracy TXRU
TXRU
Narrow BW (e.g. 5/10 MHz) RXRU
RXRU
…
E.g. 16, 32 RXRUs
Hybrid Transceiver
Digital narrowband receiver
Complement wideband, , high accuracy and cost hybrid transceiver with digital narrowband, low cost receiver to enhance system operation
RXRU
RXRU

## Slide 6: Proposal
Support enhancing hybrid architecture operation using digital RX subsystem consisting of the same (or similar) amount of RxRUs as the number of antenna elements.
UL Signal design and UL control channel design needs to follow the following principles:
  Transmission bandwidth of the UL control signal and associated demodulation UL RS is significantly smaller than the system bandwidth, e.g. 10/20 MHz bandwidth.
  UL Signal design to enable high multiplexing capability for the UL control signals like scheduling request.
  Efficient joint operation of hybrid RX and digital RX, e.g. efficient utilization of UL data and UL control channels.