## Slide 1
WF on interference measurement in Rel-14
3GPP TSG RAN WG1 #86 R1-167968
Gothenburg, Sweden 22nd- 26th August, 2016
Agenda item: 7.2.4.2.3
Huawei, HiSilicon, Deutsche Telecom, China Telecom, CATT

## Slide 2: Background
The agreement from RAN1#85 is
  Also, interference measurement enhancement can be considered
When both intra-cell and inter-cell interference are captured, significant gain is observed, i.e.
Source | Cell Average Gain | Cell Edge Gain | Simulation Assumptions
Huawei[R1-167674] | 25% | 36% | Both intra-cell and inter-cell interference captured with realistic error modeling
Ericsson[R1-167642] | 18% | 21% | Both intra-cell and inter-cell interference captured with ideal link adaptation
CMCC[R1-167093] | 9% | 14% | Only intra-cell interference captured in simulation
NTT DCM[R1-167350] | 3% | 9% | 

## Slide 3: Proposals
Specify interference measurement enhancements in Rel-14.
Possible schemes including:
  Aperiodic CSI-IM
  Definition and configuration of a new type CSI-IM for TM9 and TM10
    Interference measurement is based on cancellation of intended signals
    Both inter-cell and intra-cell interference should be captured
    FFS NZP CSI-RS or DMRS
  If needed, L1/RRC signaling to assist UE interference measurement
  In addition, a smaller value of nCQI_ref (e.g. 2) can be supported