## Slide 1: WF on support of larger maximum TBS and channel bandwidth for FeMTC
Intel, Spreadtrum, Huawei, HiSilicon, Ericsson,
3GPP TSG RAN WG1 Meeting #86 R1-168057
Gothenburg, Sweden, 22nd – 26th August
Agenda Item: 7.2.10.1

## Slide 2: Background
Some objectives from Rel-14 FeMTC WID [RP-161321]
The objective is to specify the following improvements for machine-type communications for BL/CE (eMTC) UEs
  Larger maximum TBS
  Larger max. PDSCH/PUSCH channel bandwidth in connected mode at least in CE mode A in order to enhance support e.g. voice and audio streaming or other applications and scenarios
Use cases
To support widespread application of eMTC technology for wearables and other devices that benefit from small form-factor, low power consumption, and enhanced coverage, but support higher-data rate applications including HD voice and multimedia calls, audio/video streaming, health monitoring, etc., data rates greater than those offered by Rel-13 eMTC are necessary.
Observation
To realize meaningful gains in data rates without sacrificing coverage, the max. TBS and the max. channel BW for PDSCH and PUSCH should be increased.

## Slide 3: Proposals
    For Rel-14 FeMTC UEs, the maximum UL TBS for CEMode A UEs with maximum 1.4 MHz bandwidth in TDD/HD-FDD is increased to 3240 bits.
    Idle mode operations reuse the Rel-13 eMTC design
    For Rel-14 FeMTC UEs, the larger UE channel BW for PDSCH and PUSCH in RRC connected mode, at least in CEMode A, is 5 MHz.
    For Rel-14 FeMTC UEs supporting larger UE channel BW for PDSCH and PUSCH, the larger max. UL and DL TBS is 3240 bits.
  For Rel-14 FeMTC UEs with larger TBS and channel BW:
    Idle mode operations reuse the Rel-13 eMTC design