## Slide 1: WF on multi-carrier UL LBT operation
Huawei, HiSilicon
3GPP TSG RAN WG1 #86 R1-168078
Gothenburg, Sweden
22nd – 26th Aug 2016
Agenda item: 7.2.1.3
Document for decision

## Slide 2: Background for DL multi-carrier operation
Type A: each carrier maintains contention window size (CWS) independently and performs a Cat-4 channel access procedure.
  Type A1: Independent backoff counter per carrier is used. If the absence of any other technology sharing the carrier cannot be guaranteed on a long term basis (e.g. by level of regulation), after the eNB ceases transmission on any carrier, the eNB can resume decrementing the counter either after waiting for 4 CCA slots or after reinitializing the counter.
  Type A2: The counter for each carrier is generated using the maximum CWS among all the carriers, and the counter is reinitialized after a transmission on any carrier.
Type B: one carrier is selected randomly or semi-statically from the group of carriers to perform Cat-4 LBT before transmission, other carriers can start transmission simultaneously if it succeeds with a 25us LBT before the transmission.
  Type B1: a single CWS is maintained for the group of carriers, and the CWS adaptation is based on the HARQ-ACK feedback on all the carriers within the group.
  Type B2: CWS is maintained independently on each carrier based on the HARQ-ACK feedback on that carrier only. The random counter for the Cat-4 LBT on the selected carrier is chosen based on the maximum CWS among all the carriers.

## Slide 3: Background for eLAA MCOT sharing
Current eLAA agreement for MCOT sharing
  For the DL and UL transmissions occurring on the same channel, an eNB starting the DL transmission based on a Cat 4 LBT with a given MCOT, can share its channel occupancy with its UEs such that the total transmission duration by the eNB and UEs does not exceed the MCOT limit.

## Slide 4: Proposal
For UL multi-carrier LBT, UE performs UL LBT according to the LBT indication from the eNB.
UL CWS is maintained independently for each carrier.
An eNB starting the DL transmission based on Type B multi-carrier LBT acquiring a given MCOT, can share its channel occupancy with its UEs on all the carriers completing Type B LBT.
  The channel occupancy is started with a DL transmission after the carrier performing Cat.4 LBT completes Cat.4 LBT;