## Slide 1: WF on Implementation complexity for eMBB coding scheme
3GPP TSG RAN WG1 Meeting #86 R1-16XXXX
Gothenburg, Sweden, 22nd – 26th August 2016
Agenda Item: 8.1.4.1
Nokia, ASB, Samsung, Ericsson, LG ….

## Slide 2: Background
High area and energy efficiencies are required to fulfill eMBB requirements
Maximum baseband power of a smartphone is in the range of 1-3 W. Assuming maximum 1W is available for decoding, we would require less than 50 pJ/bit energy efficiency to deliver 20 Gbps peak data rates.
For UEs, limited chip area is typical assumption in many implementation efforts on turbo codes.

## Slide 3: Background
Evaluation of the eMBB DL coding schemes should be consistent with the implementation complexity analysis.
  Decoding algorithms used in the performance evaluations should be verified with the implementation complexity details.
  Trade-off between flexibility and complexity can be determined.
  Latency aspects can often be found or acquired by the implementation throughputs.
  Benefits of having exact coding constructions should be identified with the implementation complexity.

## Slide 4: Observations
Observations on eMBB coding scheme
Turbo implementations efforts show inferior area and energy efficiencies for supporting 20 Gbps peak data rate with limited baseband power at the UE.
Multiple code rate single block size LDPC have considerably good implementations due to parallelized architecture and flexibility of code design, and suitable to fulfil NR requirements. Flexible LDPC shows inferior area efficiency than inflexible LDPC.
Polar coding implementations are relatively immature, where implementations efforts are only available for successive cancelation, iterative decoding, and SCL with lower list sizes (<4).