## Slide 1: WF on CSI timing relationship
LG, InterDigital, Intel, Huawei
R1-168135
3GPP TSG RAN1 #86
Gothenburg, Sweden, Aug 22 – 26, 2016
Agenda Item: 8.1.5

## Slide 2: Background
In NR, more compact and flexible CSI procedure is desirable for forward compatibility and minimizing CSI aging.
However, implementation aspects should be taken into account especially for setting CSI reporting timing so that flexible CSI feedback timing is required.
  The time gap between RS transmission and CSI reporting is dependent on
    Propagation delay
    UL timing advance
    CSI computation delay
  CSI computation delay is further dependent on
    CSI contents (e.g. implicit, explicit, with/without PMI, etc.)
    CSI granularity (e.g. size of codebook, range of rank, etc.)
    Number of CSI processes

## Slide 3: Proposals
Study flexible timings of RS indication/transmission for CSI measurement, CSI feedback triggering/reporting. Following aspects should be considered at least for aperiodic/SPS CSI reporting;
  Linkage between each timing
    Ex1) RS indication and CSI feedback triggering at the same SF
    Ex2) RS indication and RS transmission at the same SF
    Ex3) RS indication, RS transmission, CSI feedback triggering and CSI reporting at the same SF
  Signaling method
    E.g. implicit or explicit signaling on each timing
  Feasible time gap between RS transmission and CSI reporting taking CSI computation delay, propagation delay and UL timing advance into account
  Note: Single or multiple triggering/transmission/reporting can also be considered.
    Ex1) Both single shot and multi-shot transmission of RS
    Ex2) Both single SF and multi-SF CSI reporting
  Note: Timings of RS indication and CSI feedback triggering above indicates layer 1 control signaling.
  Note: RS indication can be RS triggering or RS activation/deactivation, and can include RS resource configuration.
  Note: This doesn’t preclude a fixed timing based RS transmission for CSI measurement, CSI feedback reporting.