## Slide 1: WF on Channel Code Evaluation for URLLC Evaluation
Qualcomm Incorporated
3GPP TSG RAN WG1 #86 R1-16xxxx
Gothenburg, Sweden, Aug 22 - 26, 2016
Agenda item: 8.1.4.1

## Slide 2: Background
Previous agreement on URLLC assumed very low code rate and MCS not typically used
URLLC system and link evaluations may consider efficient link adaption and procedures
Groups within each agenda item may be mis-aligned (e.g., 200 Byte transmision)
From RAN1 #85

## Slide 3: Way Forward
URLLC code rates and payload sizes for evaluation should be expanded (and overlap with EMBB)
Channel* | AWGN |  |  |  | 
Modulation | QPSK, 16 QAM |  |  |  | 
Coding Scheme | Convolutional Codes | Turbo | LDPC | Polar | 
Code rate | 1/6, 1/3, 2/5, 1/2, 2/3, 3/4, 5/6 |  |  |  | 
Decoding algorithm** | Viterbi | Max-log-MAP | BP or BP approx. |  | List-X
Info. block length*** (bits w/o CRC) | 20,40,200,600,1000,2000 |  |  |  | 
Light blue from URLLC/MMTC