## Slide 1
Way Forward on RB grid definition for mixed numerologies
ZTE, ZTE Microelectronics, Ericsson, Qualcomm, Nokia, Alcatel-Lucent Shanghai Bell, Panasonic, Convida Wireless
R1-168309
3GPP TSG RAN WG1 #86
Gothenborg, Sweden, 22th – 26th August 2016
Agenda item 8.1.3.1

## Slide 2
Background
Agreements:
In one carrier when multiple numerologies are time domain multiplexed,
  RBs for different numerologies are located on a fixed grid relative to each other
  For subcarrier spacing of 2n * 15kHz, the RB grids are defined as the subset/superset of the RB grid for subcarrier spacing of 15kHz in a nested manner in the frequency domain
  Note that following numbering in the figure is just an example
  FFS: frequency domain multiplexing case

## Slide 3: Proposal
Add one bullet to the Agreement
Agreements:
The RB grid for a numerology assumed for transmission does not change dynamically over time
In one carrier when multiple numerologies are time domain multiplexed,
  RBs for different numerologies are located on a fixed grid relative to each other
  For subcarrier spacing of 2n * 15kHz, the RB grids are defined as the subset/superset of the RB grid for subcarrier spacing of 15kHz in a nested manner in the frequency domain
  Note that following numbering in the figure is just an example
  FFS: frequency domain multiplexing case