## Slide 1
3GPP TSG RAN WG1 Meeting #86 R1-168360
Gothenburg, Sweden, 22nd - 26th Aug 2016
Agenda item: 8.1.5
WF on QCL assumptions & configurations in NR
Huawei, HiSilicon, China Telecom, DoCoMo, CATR, Intel

## Slide 2: Background
The following agreements have been reached at RAN1#85:
  Study necessity of QCL and measurement assumptions for antenna ports in NR
  It should be possible as one option to assume QCL between ports of two different panels of the same transmission points

## Slide 3: Proposal
The following should be supported:
  By default NR will have no QCL assumption among all antenna ports unless specified or indicated (as in LTE since Rel-11)
  The study should explicitly specify or indicate all needed QCL assumptions
  Multiple QCL configurations should be supported by NR
    Note: QCL configurations are defined as the different sets of large-scale channel properties.