## Slide 1: WF on beam management
CATT, Samsung, National Instruments, ZTE, [CMCC]
3GPP TSG RAN WG1 Meeting #86 R1-168388
Gothenburg, Sweden, August 22nd - 26th 2016
Agenda Item: 8.1.5

## Slide 2: Background
Channel [beam] reciprocity
  Holds for both TRP and UE
  Does not hold for TRP and UE
  Holds for TRP but does not hold for UE
  Does not hold for TRP but holds for UE

## Slide 3: Background
Definition: A beam pair consists of one Tx beam and one Rx beam in one link direction

## Slide 4: Proposal(1)
Consider different channel reciprocity assumptions in beam management procedures
  At a TRP or UE, with TX and RX channel reciprocity (full or partial) (e.g., beam reciprocity), TX beam (or RX beam) can be obtained from RX beam (or TX beam) to reduce overhead and latency
  Without TX and RX channel reciprocity, beam management procedure may require TX and RX beam sweeping in both DL and UL links

## Slide 5: Proposal(2)
RAN1 study different methods of determining a beam pair for communication, e.g.,
  Joint determination: Tx beam and Rx beam of the beam pair are determined jointly. In example figure below, different colors represent different TRP TX beams
  Separate determination: Tx beam or Rx beam of the beam pair are determined sequentially. In example figure below, set of symbols with same color represent same TRP TX beam and different colors represent different TRP TX beams
t
t
UE Rx beam sweeping region
TRP Tx beam sweeping region
TRP Tx and UE Rx beam sweeping region

## Slide 6: Proposal(3)
Study beam management procedure with and without explicit signaling of beam(s) or beam group(s) used for transmission