## Slide 1
WF on some definition of terminologies for “autonomous/grant-free/contention-based” MA
LG Electronics, ETRI, …
R1-168423
3GPP TSG RAN WG1 #86
Gothenburg, Sweden, 22nd – 26th August 2016
Agenda item 8.1.2.2

## Slide 2: Background
During previous meetings, following agreements on NoMA are made:
Agreements in RAN1 #85
  Autonomous/grant-free/contention based UL non-orthogonal multiple access has the following characteristics
    A transmission from UE does not need the dynamic and explicit scheduling grant from eNB
    Multiple UEs can share the same time and frequency resources
  For autonomous/grant-free/contention based UL non-orthogonal multiple access, the following should be studied
    Collision of time/frequency resources from different UEs, solutions potentially including
      E.g., code, sequence, interleaver pattern
    UL synchronization (DL synchronization assumed)
      Case 1: Timing offsets between UEs are within a cyclic prefix
      Case 2: Timing offsets between UEs can be greater than a cyclic prefix, FFS the exact model of timing offsets
    Requirement for power control
      Case 1: Perfect open-loop power control, i.e., equal average SNR between UEs for potentially link level calibration
      Case 2: Realistic open-loop power control with certain alpha and P0 values
      Case 3: Close-loop power control
    Receiver impact
For “autonomous/grant-free/contention-based” MA, the terminology of ‘Resource and Signature’ in relation to MA is NOT defined.

## Slide 3: Proposal
For “autonomous/grant-free/contention-based” MA, following terminologies are defined:
  Physical Resource Zone
    Common physical time/frequency resources where one or more UEs use for UL transmission
  MA Signature pool
    A set of multiple signatures that multiple UE can share for UL transmission
    A set of multiple signatures to differentiate UL transmissions of multiuser signals
      e.g., Time/frequency/codebooks/sequences/interleaver patterns
  MA Signature
    Specific identification/recognition that a UE selects/uses for UL transmission
      e.g., a time/frequency/code/codebook/sequence/interleaver pattern
      Note: Here, the identification does not mean UE specific ID
  Note: MA Signature and MA Signature pool are separators/recognizers for MUD

## Slide 4: Appendix 1: Physical Resource Zone
An example of Physical Resource Zone
An example of Physical Resource Zone in LTE (RACH type 1)
  Physical Resource Zone for RACH type 1 is defined by 6 RBs and 1 subframe
Physical Access Zone
Freq.
Time
…
System
Bandwidth
x RBs
y subframes

## Slide 5: Appendix 2: MA Signature Pool
Examples of MA Signature Pool
An example of MA Signature Pool in LTE (RACH type 1)
  MA Signature Pool for RACH type 1 is defined by 64 Preambles
Freq.
Time
Time Signature 2
Time Signature 1
A Time Signature Pool (including 7 Time Signatures)
A Time/Frequency Signature Pool (including 56 Time/Freq. Signatures)
A Code Signature Pool (including 3 Code Signature)
Freq.
Time
Time/Freq. Signature 2
Time/Freq. Signature 1
Freq.
Time
Code Signature 2
Code Signature 1

## Slide 6: Appendix 3: MA Signature
Examples of MA Signature
An example of MA Signature in LTE (RACH type 1)
  MA Signature for RACH type 1 is defined by 1 Preamble which is selected by a UE
Freq.
Time
Time Signature 2
Time Signature 1
Freq.
Time
Time/Freq. Signature 2
Time/Freq. Signature 1
Freq.
Time
Code Signature 2
Code Signature 1
A Time Signature Pool (including 7 Time Signatures)
A Time/Frequency Signature Pool (including 56 Time/Freq. Signatures)
A Code Signature Pool (including 3 Code Signature)