## Slide 1: Harmonized WF on Pools Configuration (again)
Ericsson
3GPP TSG RAN WG1 Meeting #86 R1-168506
22nd – 26th August, 2016 Gothenburg, Sweden
Agenda item: 7.2.2.2.3

## Slide 2: Proposal
V2V pool is defined by a cyclically repeating bitmap mapped to all UL subframes except for at least SLSS subframes which are skipped
  E.g., the bitmap length is 20
  FFS if/how to handle the case where the bitmap does not repeat an integer number of times within the DFN period
The bitmap defines which subframes are allowed for V2V SA/data transmission and/or reception for a given zone (i.e., for a pool)

## Slide 3: Example
SLSS configured on SF nr 2 (counting from 0)
Pool bitmap: [1 0 1 1 1]
V2V logical index per physical subframe: [0 1 nd 2 3 4 5 6 7 8 9 … ]
Note that V2V transmission is only allowed for the red subframes